Rule of thumb: empty airframe (wings, fuselage, tail) weight will be about 40-50% of the All-Up Weight (AUW).

This checks out with commercial quadcopters like the DJI AGRAS T40 which has an empty weight of around 38kg and can carry 50kg of (equipment and payload). This also checks out with the XAG P100 quadcopter which has an empty weight of about 33kg and can carry 88kg of (equipment and payload).

Batteries rule of thumb: Batteries for these two platforms above are around 7kg. Which is 20% of their empty weight. But these are quadcopters. I need to search for fixed wing platforms to have a better idea.

A great example/design is this one:
https://www.buildyourowndrone.co.uk/finwing-sabre-arf

And this one:
https://en.wikipedia.org/wiki/AeroVironment_Switchblade

with an all up weight of 5kg. Hand launchable. Unoptimized for sure. I definitely think it could become smaller, faster and compact.

Software:
XFLR5 for wing design
Autodesk Fusion (personal use)

Center of gravity is super important. As we already know from simulation..

Step	Goal	Key Software	Key Metric / Outcome
1	Weight & Requirements	Spreadsheet (Google Sheets, Excel)	Target All-Up Weight (AUW)
2	Aerodynamic Design	XFLR5	Wing Area (S), Stable Static Margin (5-15%)
3	Mechanical Design	Autodesk Fusion 360	A buildable 3D model, Correct Center of Gravity (CG)
4	Propulsion System	eCalc	Motor/Prop/Battery combo, Thrust-to-Weight (>0.7), Flight Time
5	Build & Test	3D Printer, Hand tools	A physical, working UAV

And repeat

I need to find the payload weight first.

Bionic Morphing wings? Too far fetched? Might work.

Davis recoiless gun. This one is great. Should consider.

Great video:
https://www.youtube.com/watch?v=x4bHc4X5Ilw

ZOHD company is very interesting: https://www.zohd.net/planes

Let us copy something like this for starters:
https://www.zohd.net/zohd-dart-xl-extreme

RC companies use slightly forward swept wings to balance nose weight. I think the initial design should be like this. Because it also looks cool and stable. And we will see for later. Our camera will be in the front as well. The computer probably also.

Related publication by ELKAK:

https://www.elkak.gr/information-requests

Emphasize weak spots and vulnerabilities in large UAS. Our system can shoot where it must.

Design Decision process:
Pick an MTOW that can realistically include the payload + structure + propulsion + energy; then pick a wing area from a target stall speed (and available CLmax​), and finally pick aspect ratio to get span/chords. Here’s a clean, practical way to do it for a 2 kg “clean” payload.
# 1) First, a reasonable MTOW
For small electric fixed-wing UAVs, payload fraction is typically 20–35% depending on endurance. For a 2 kg payload, a good starting MTOW is ~6.0 kg (short–medium endurance) with a plausible mass breakdown:
- Payload: 2.0 kg
- Structure/airframe + landing gear: 1.2–1.5 kg
- Propulsion (motor, ESC, prop, servos): 0.5–0.7 kg
- Avionics (flight computer, RX, GPS/INS, pitot), camera, Jetson Orin Nano (~170 g): 0.5–0.7 kg
- Battery (for ~40–60 min cruise): 0.5–0.8 kg (energy depends on your drag & cruise power; see note at end)
This lands near MTOW ≈ 6 kg. If you need >90 min endurance, expect MTOW to climb.
# 2) Pick stall speed → wing loading → wing area
Choose a gentle stall for hand/belly launch and short landing: say  m/sVs​=10 m/s (≈ 36 km/h). With a typical small-UAV airfoil without flaps, take CLmax​≈1.6.
Use
S=ρVs2​CLmax​2W​
where W=MTOW⋅g,  ρ=1.225 kg/m3.
For MTOW = 6.0 kg:
- S≈0.60 m2
- Wing loading  kg  W/S≈6.0 kg/0.60 m2=10 kg/m2 (≈ 98 N/m²), very reasonable for a small UAV.
(If you can accept  m/sVs​=12 m/s, S drops to ~0.42 m²; takeoffs/landings get hotter.)
# 3) Choose aspect ratio → span & mean chord
Aspect ratio AR of 8–10 is a sweet spot (manufacturable, efficient).
- With  S=0.60 m2 and AR=9:
  - Span  b=AR⋅S​=9⋅0.60​≈2.32 m
  - Mean aerodynamic chord  cˉ=S/b≈0.26 m
Give the wing some taper (e.g., taper ratio λ=ctip​/croot​≈0.5) for lower induced drag and better tip stall behavior:
- Root chord  cr​≈cˉ⋅1+λ2​≈0.26⋅1.52​≈0.35 m
- Tip chord  ct​=λcr​≈0.18 m
# 4) Sweep & dihedral
- Sweep: keep it simple—0–5° leading-edge sweep. Small sweep eases CG packaging without hurting CLmax​.
- Dihedral: 2–3° per panel for roll stability.
- Tail volume: (if conventional tail) horizontal tail volume coefficient VH​≈0.5–0.7 and vertical VV​≈0.03–0.05 are good starting targets; size tail after estimating the fuselage moment arm.
# 5) Power and prop (order-of-magnitude)
- Thrust-to-weight for launch/climb: T/W≈0.3–0.4 is comfy. For 6 kg: ~18–24 N static thrust.
- Electrical power (max): 600–900 W class outrunner/inrunner on 6S–8S with a 13–15″ prop (final choice depends on your drag and pitch speed).
- Cruise power: many 5–7 kg fixed-wings cruise on 120–220 W. For 60 min at 170 W bus power, energy ≈ 170 Wh → battery mass ~0.7 kg if using Li-ion at ~240 Wh/kg (plus margins). Scale endurance roughly linearly with Wh.

## A concrete “baseline” you can build around
- MTOW: ~6.0 kg
- Clean payload: 2.0 kg
- Wing area S: 0.60 m² (targets  m/sVs​≈10 m/s with CLmax​≈1.6)
- Aspect ratio: 9
- Span b: ~2.32 m
- Root chord cr​: ~0.35 m
- Tip chord ct​: ~0.18 m (taper ≈ 0.5)
- Sweep (LE): ~5° (or 0° if you prefer simple build)
- Dihedral: ~2.5° per panel
- Target max power: ~800 W
- Battery for ~1 h cruise: ~0.6–0.8 kg Li-ion, ~150–200 Wh usable (include 20% reserves)
### Variants (quick swaps)
- Slower, softer ops: If you want  m/sVs​≈9 m/s, bump S to ~0.74 m² → with AR = 9: b≈2.58m, cˉ≈0.29m.
- Faster, smaller wing: For  m/sVs​≈12 m/s, S≈0.42m2 → with AR = 9: b≈1.94m, cˉ≈0.22m (launch/landing hotter).

## Why not “just” pick wing loading?
Wing loading alone doesn’t guarantee a viable airplane because:
1. Stall speed depends on W/S and CLmax​.
2. Endurance and takeoff distance depend on drag/power, not just area.
3. Structural and packaging constraints (battery volume, prop clearance, CG with your 2 kg payload and Jetson) drive geometry choices (taper, sweep, tail arm).
If you share your desired endurance, launch/landing method, and cruise speed/altitude, I can lock these numbers tighter and give you a full first-cut weight & power budget plus airfoil suggestions.

Also this dude describes his process in detail:
https://www.youtube.com/watch?v=yQ80AqMJxUg

To watch:
https://www.youtube.com/watch?v=akIrS6M-2PQ&t=5s
https://www.youtube.com/watch?v=y2qwLbV4C64